## Slide 1: Module 2: Hardware Description Language
Computer Organization (CS220)
Semester 2022-23-II
Urbi Chatterjee
CSE, IIT Kanpur

## Slide 2: Computer Aided Digital Design
Small Scale Integration  Medium Scale Integration  Large Scale Integration  Very Large Scale Integration
CAD
  Verification and Design
  Automatic Placement and Routing of Circuit Layout
SSI--- 0-12 GATE MSI---12-100 GATE LSI---100-1000 GATE VLSI---1000-10000 GATE
SoCs: Million gates, Software and Hardware

## Slide 3: Emergence of HDLS
Programming Languages
C, Pascal, Fortran
Describe computer programs that are sequential in nature.
Hardware Description Languages (HDLs)
Verilog, VHDL
Describe digital circuits that are concurrent in nature.
They
Verilog was originated in 1983 at Gateway Design Automation; whereas VHDL was developed by Defense Advanced Research Projects Agency (DAPRA) around 1987.
CAD Tools are used to simulate large digital designs and verify the logic.

## Slide 4: Contribution to Logic Synthesis
Hurdle: manually translate the HDL based design into a schematic circuit with interconnection between the gates.
Digital Circuits are described at a register transfer level (RTL) by HDL.
It specifies how the data flows between the registers and how the design processes the data.
The details of the gates and their interconnects to implement the circuit were automatically extracted by the logic synthesis tool from the RTL description.
HDL
Simulate
Synthesize
Abstraction in functionality and data flow
Logic Synthesis tool automatically implement in terms of gate and interconnects.

## Slide 5: Platforms that can be simulated
System Boards
Interconnect Buses
Field Programmable Gate Arrays (FPGAs)
Programmable Array Logics (PALs)

## Slide 6: Typical Design Flow for VLSI IC circuit
Design Specification
Behavioral Description
RTL Description
Functional Verification and Testing
Gate Level Netlist
Logic Verification and Testing
  Floor Planning, Automatic Place and Route
Layout Verification
Implementation

## Slide 7: Typical Design Flow for VLSI IC circuit
Design Specification: Abstract Description of the overall Architecture
Behavioural Description: Analyse the design in terms of functionality, performance, complience with Standards
RTL: Data flow description
Functional Verification and Testing: Checks sanity
Logic Synthesis: Convert RTL to gate level netlist
Logic Verification: Whether it meets time, are and power specification
Floor Planning, Automatic Place and Route: Convert gate level netlist to layout
Layout Verification: Check Sanity
Implementation: Can be used to be fabricated in a chip.

## Slide 8: Design Methodologies
Top Level Block
Sub Block 1
Sub Block 2
Leaf Cell
Leaf Cell
Leaf Cell
Leaf Cell
Top Down Approach
Top Level Block
Macro cell 1
Leaf Cell
Leaf Cell
Leaf Cell
Leaf Cell
Macro Cell 2
Bottom Up Approach
Design Architect: Specifications of top level block
Logic designers: Breaks up the functionality among blocks and sub-blocks
Circuit Designers: optimise leaf cells and build high level cells
Switch-level Designers:
create library of leaf cells using switches

## Slide 9: Stimulus Block (Test Bench)
Used for simulation
Apply stimulus and check results
Better to keep the stimulus and design blocks separate
Can be written in Verilog.
Stimulus Block
Design Block
Top Level Block
Stimulus Block
Design Block

## Slide 10: Always Block
Executed at some particular event
Event is defined by a sensitivity List
Statements inside an always block are executed sequentially
Can be used to realised combinational or sequential elements.

## Slide 11: Initial Statement
Initial keyword makes the circuit perform a set of operations, but only when the circuit starts.
It occurs only once.
It is useful for initializing circuit elements.

## Slide 12: Basic Constructs and Conventions
Comments:
  /* This is Urbi’s Program*/
  /* I am showing /* a bad example */ of comments */
  /* But this is // absolutely Legal */
Operators:
  A=~B; //unary
  A=b&c; //binary
  A=b?c:d; //ternary
Number Representation:
4’b0101 (4 bit binary)
12’h98a (12 bit hex)
Sized Number
23456
‘hDF
Un-Sized Number
reg value;
Keyword
Identifier

## Slide 13: Value Set
0: logic zero, false condition
1: logic one, true condition
x: unknown logic value
z: high impedence, floating state

## Slide 14: Wire and Reg
Wire is used for combinational logic.
Wire can not store a value.
A wire can be assigned a value by an “assign” statement.
Default datatype is wire which is 1 bit.
Reg can store value.
Reg can drive strength.
Reg can be used for modelling both combinational and sequential logic.
Reg can be driven from initial and always block.

## Slide 15: Wire and Reg
D FlipFlip
AND
clk_wire
in_wire
d_wire
q_reg
q_bar_reg
clk
q
q_bar

## Slide 16: Wire vs Reg
module wire_example(a,b,y);
input a,b;
output y;
wire a,b,y;
assign y=a&b;
endmodule
module reg_combine_example(a,b,y);
input a,b;
output y;
reg y;
wire a,b;
always@(a or b)
begin
y=a &b;
end
endmodule

## Slide 17: Register Design
D FlipFlip
q
q_bar
clk
d
Reset
module reg_seq_example(clk, reset,d,q);
input clk, reset,d;
output q;
reg q;
wire clk, reset, d;
always @(posedge clk or posedge reset)
if (reset) begin
q<=1'b0;
end
else begin
q<=d;
end
endmodule

## Slide 18: Thank you.