## Slide 1: MODULE 3:The Basics of Logic Design
Computer Organization (CS220)
Semester 2022-23-II
Urbi Chatterjee
CSE, IIT Kanpur

## Slide 2: Gates, Truth Tables, and Logic Equations
Modern digital computers
Signals
  Asserted
  Deasserted
Logic Blocks
  Combinational: A logic system whose blocks do not contain memory and hence compute the same output given the same input.
  Sequential: A group of logic elements that contain memory and hence whose value depends on the inputs as well as the current contents of the memory.

## Slide 3: Representation of LOGIC BLOCKS: TRUTH TABLE
Truth Tables can be used to describe any combinational logic function. Each entry specifies the value of all the outputs for that particular input combination.

## Slide 4: Representation of LOGIC BLOCKS: LOGIC EQUaTIONS
 | 00 | 01 | 11 | 10
0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
D=A+B+C
 | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
E=A’.B.C+A.B’.C+A.B.C’
 | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
F=A.B.C

## Slide 5: LOGIC GATES

## Slide 6: 2-to-4 DECODER
2-to-4 DECODER
A1
A0
E
Y0
Y1
Y2
Y3

## Slide 7
Enable | INPUTS |  | OUTPUTS |  |  | 
E | A1 | A0 | Y3 | Y2 | Y1 | Y0
0 | x | x | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0
Y3=E.A1.A0
Y2=E.A1.A0′
Y1=E.A1′.A0
Y0=E.A1′.A0′

## Slide 8
Can we design a 3-to-8 decoder using 2-to-4 decoders?
Check yourself!

## Slide 9: Full Adder
FULL ADDER
A
B
Cin
Cout
S

## Slide 10
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 11
 | 00 | 01 | 11 | 10
0 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0
 | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1
S=A’.B’.Cin+ A’.B.C’in+ A.B’.C’in+A.B.Cin
Cout=A’.B.Cin+ A.B’.Cin+ A.B.C’in+A.B.Cin
Sum of Products
(It gives HIGH-1 output.)
Products of Sums
(It gives LOW-0 output.)
S=(A+B+C’in). (A+B’+C’in). (A’+B+Cin).(A’+B’+C’in)
Cout=(A+B’+C’in). (A’+B+Cin). (A’+B’+Cin).(A’+B’+C’in)

## Slide 12: programmable logic array and Two Level Logic
sum-of-products representation
A PLA has a set of inputs and corresponding input complements (which can be implemented with a set of inverters), and two stages of logic.
The first stage is an array of AND gates that form a set of product terms (sometimes called minterms); each product term can consist of any of the inputs or their complements.
The second stage is an array of OR gates, each of which forms a logical sum of any number of the product terms.

## Slide 13: programmable logic array and Two Level Logic

## Slide 14: EXAMPLE

## Slide 16: read-only memory (ROM)
A ROM is called a memory because it has a set of locations that can be read; however, the contents of these locations are fi xed, usually at the time the ROM is manufactured.
Programmable ROMs (PROMs) , Erasable PROMs (EPROMs)
A ROM has a set of input address lines and a set of outputs.
The number of Addressable entries in the ROM determines the number of address lines.
If the ROM contains 2m addressable entries, called the height, then there are m input lines.
The number of bits in each addressable entry is equal to the number of output bits and is sometimes called the width of the ROM.
The total number of bits in the ROM is equal to the height times the width. The height and width are collectively referred to as the shape of the ROM.

## Slide 17: EXAMPLE: ROM for 2-to-4 Decoder
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 0