## Slide 1: Module 2: Hardware Description Language
Computer Organization (CS220)
Semester 2022-23-II
Urbi Chatterjee
CSE, IIT Kanpur

## Slide 2: Blocking and Non-Blocking Statements
Blocking statements must be executed before the executions of the statements that follow it in a sequential block.
Non-blocking statements can be used to schedule assignments without blocking the procedural flow.
It is best to use non-blocking statements when multiple reg assignments within the same step of time is required. It is independent of the order or inter-dependence on each other.

## Slide 3: Blocking and Non-Blocking Statements
module block_non_block()
reg a, b, c, d, e, f;
initial begin
a = #1 1'b1;
b = #2 1'b0;
c = #5 1'b1;
end
initial begin
d <= #1 1'b1;
e <= #2 1'b0;
f <= #5 1'b1;
end
endmodule
assignment will be done at time 1
assignment will be done at time 3
assignment will be done at time 8
assignment will be done at time 1
assignment will be done at time 2
assignment will be done at time 5
Blocking
Non-Blocking
Check how blocking and non-blocking statements act in an always block?

## Slide 4: System Tasks
Verilog provides standard system tasks for certain routine operations.
Syntax: $<keyword>
Display Information:
input to the system tasks are: variables, signal names or quoted strings
Monitoring:
Monitoring mechanism is used to monitor a signal when its value changes. Can be used in stimutus block for debugging.
stop and finish tasks:
$display (p1, p2, ..., pn)
$monitor (p1, p2, ..., pn)
  #100 $stop;
  #800 $finish;

## Slide 5: Compiler Directives
used to define text macros.
To include the contents of a verilog source file in another verilog file during compilation.
`define
`include
`define WDRD_SIZE 32;
`define F $finish;
`include myfile.v
...
...
<verilog code in new_design.v>
...
...

## Slide 6: Ranges
module my_mux(X,Y,S,M);
input [2:0] X,Y;
input S;
output[2:0] M;
assign M[0]=X[0] & ~S | Y[0] & S;
assign M[1]=X[1] & ~S | Y[1] & S;
assign M[2]=X[2] & ~S | Y[2] & S;
endmodule
Precedence: https://class.ece.uw.edu/cadta/verilog/operators.html

## Slide 7: Components of a Verilog Module
Module Name, Port List, Port Declaration, Parameters
Declaration of Wires, regs and other variables
Instantiation of lower level modules
Data flow statements (assign)
Always and initial blocks
Tasks and Functions
Endmodule statement
Width mismatch
Unconnected port

## Slide 8: For Loop in Verilog
Initial keyword makes the circuit perform a set of operations, but only when the circuit starts.
It occurs only once.
It is useful for initializing circuit elements.
reg [15:0] memory[255:0];
interger index;
initial
begin
for (index=0; index<16; index=index+1)
begin
memory[index]=0;
end
end

## Slide 9: Design Example: 8 bit Left Shift Register
module lshift_reg(clk, rstn, load_val, load_en, op);
input clk, rstn, load_en;
input [7:0] load_val;
output reg [7:0] op;
always @ (posedge clk)
begin
if (!rstn)
begin
op<=0;
end
else
begin
if(load_en)
begin
op<=load_val;
end
else
begin
op[0] <= op[7];
op[1] <= op[0];
op[2] <= op[1];
op[3] <= op[2];
op[4] <= op[3];
op[5] <= op[4];
op[6] <= op[5];
op[7] <= op[6];
end
end
end
endmodule

## Slide 10: Design Example with FOR: 8 bit Left Shift Register
module lshift_reg(clk, rstn, load_val, load_en, op);
input clk, rstn, load_en;
input [7:0] load_val;
output reg [7:0] op;
always @ (posedge clk)
begin
if (!rstn)
begin
op<=0;
end
else
begin
if(load_en)
begin
op<=load_val;
end
else
begin
for(i=0;i<7;i++)
begin
op[i+1]<=op[i];
end
op[0]<=op[7];
end
end
end
endmodule

## Slide 11: Test Bench
module test_lshift_for; //inputs and outputs reg clk, rstn, load_en; reg[7:0] load_val; wire[7:0] op; // Instantiate the Unit Under Test (UUT)
lshift_reg_for uut ( .clk(clk), .rstn(rstn), .load_en(load_en), .load_val(load_val), .op(op));
initial begin
clk<=0;
forever #10 clk<=~clk;
end
initial begin
$dumpfile("test_lshift_for.vcd");
$dumpvars(0,test_lshift_for);
rstn=0;
load_en=0;
#100;
rstn=1;
load_en=1;
load_val=8'b01010101;
#100;
rstn=1;
load_en=0;
#2000 $finish;
end
endmodule

## Slide 12: Initial Block in Test Bench
Not synthesizable
Can not converted to hardware schematic
Used to initialize variables and drive design ports
Starts at time 0 unit
Executed only once
Finishes once all the statements within the block are executed.

## Slide 13: FOR LOOP Comments
Used to replicate hardware logic in Verilog
Initial condition to specify initial values of the signals.
A check to evaluate if the given condition is true.
Update control variable for next iteration.
for(<initial_condition> ; <condition> ; <step_assignment>)
begin
//statements
end

## Slide 14: 4-Bit Ripple Carry Counter: Modules and Sub-Modules

## Slide 15
T FlipFlip
T FlipFlip
T FlipFlip
T FlipFlip
Clock
q
q
q
q
q0
q1
q2
q3
D FlipFlip
q
d
Reset
Reset
Reset | qn | qn+1
1 | 0 | 0
1 | 1 | 0
0 | 0 | 1
0 | 1 | 0

## Slide 16: 4-bit Ripple Carry Counter
module ripple_carry_counter(q, clk,reset);
output [3:0] q;
input clk, reset;
T_FF tff0 (q[0],clk,reset);
T_FF tff1(q[1),q[0],reset);
T_FF tff2 (q[2], q[1], reset);
T_FF tff3 (q[3], q[2], reset);
endmodule
module T_FF(q,clk,reset);
output q;
input clk, reset;
wire d;
D_FF dff_0 (q,d,clk,reset);
not n1(d,q);
endmodule;
module D_FF(q,d,clk,reset);
output q;
input d, clk,reset;
reg q;
always@(posedge reset or negedge clk)
begin
if(reset)
q<=1'b0;
else
q<=d;
end
endmodule

## Slide 17: TEST BENCH
module test_ripple_counter;
// Inputs
reg clk;
reg reset;
// Outputs
wire [3:0] q;
// Instantiate the Unit Under Test (UUT) ripple_carry_counter uut (.q(q), .clk(clk), .reset(reset));
initial begin
clk<=0;
forever #10 clk<=~clk;
end
initial begin
// Initialize Inputs
//clk = 0;
reset = 1;
// Wait 100 ns for global reset to finish
#100;
reset = 0;
end
endmodule

## Slide 18: Thank you.